## Slide 1
Compressor and other system component technology for R1234yf systems
Presented by Mark Mitchell Director – Global Marketing and Technical Support Unicla International Limited

## Slide 2
Technical and engineering steps to R1234yf
Following regulatory pressure, all global MVAC and vehicle manufacturer commenced the Co-operative Research Project ( CRP) for an alternative to R134a.
CRP was engineering and environmentally focussed – administered by SAE International
After extensive tests of hundreds of alternatives, R1234yf was the clear winner

## Slide 3
Technical and engineering steps to R1234yf
As a compressor manufacturer, the first challenge is to select and validate the lubricant – minimum 2000 hours of testing
Next is to check and validate the functionality of the refrigerant and how it operates in the compressor and systems where the compressor is used.
Compliance to all necessary manufacturing and safety standards

## Slide 4
Lubricant
Must meet ASHRAE standards for refrigerant suitability.
Current generation PAG and POE lubricants used in R134a found to have unacceptable chemical stability, and thermal and hydrolytic properties when used with R1234yf.
Manufactures were quick to develop suitable double end capped PAGs.
Di-capped PAG lubricants appear to be the major choice by OEMs for R1234yf, CO2 and electric drive MAC systems.

## Slide 5
Lubricant
Quality evaluation: Typical test is 2000 hrs at 500hr intervals
Compressor |  |  |  |  | Condenser |  | Evaporator | 
r.p.m | Discharge pressure kg/c㎡ | Suction pressure kg/c㎡ | Discharge temp. ℃ | Suction temp. ℃ | Temp. in ℃ | Temp. out ℃ | Temp. in ℃ | Temp. out ℃
800 | 14.0 | 3.3 | 60.1 | 17.5 | 61.1 | 48.8 | 34.2 | 20.6
2,000 | 15.4 | 2.7 | 69.6 | 16.7 | 69.7 | 51.4 | 31.7 | 19.6
3,000 | 13.2 | 1.7 | 87.0 | 14.7 | 87.6 | 50.8 | 27.3 | 7.0
3,500 | 14.0 | 1.8 | 88.4 | 17.4 | 91.1 | 52.5 | 27.4 | 8.9
1,500 | 12.9 | 2.0 | 68.0 | 12.8 | 70.0 | 52.0 | 29.0 | 9.0

## Slide 6
Lubricant
Unicla compressors use Shrieve ZEROL HD46 due
to excellent anti-wear and low hygroscopicity

## Slide 7
Refrigerant operation
Comparing R1234yf to R134a
0°C
R134a has pressure of 191.2 kpa (27.7 psi)
R1234yf is higher at 215.30 kpa (31.2 psi)
54°C
R134a has pressure of 1354.1 kpa (196.4 psi)
R1234yf is lower at 1322.7 kpa (191.7 psi)

## Slide 8
A test was carried out to provide a comparison of performance results from a common system operating on R134a refrigerant as compared against a same system converted to operate with OPTEON R1234yf refrigerant. The test comprised of the following components:
Refrigerant operation
Refrigerant | Dupont - R134a | Dupont – OPTEON R1234yf
Condenser | Kysor EC6 | Kysor EC6
Compressor | Unicla UP150 | Unicla UP150
Expansion valve | Eaton block type 2.0 ton – R134a comp. | Eaton block type 2.0 ton – R134a comp.
Hose | Burgaflex 3090 series | Burgaflex 3090 series
Hose connectors | Burgaclip with R134a service ports | Burgaclip with R1234yf service ports
Evaporator | Carrier EM14 | Carrier EM14
Lubricant | Unidap7 – PAG46 | Shrieve- Zerol HD- PAG46
Power supply | 24 volt | 24 volt

## Slide 9
Highlights:
Refrigerant operation
Test condition | Average result over 60 tests
R1234yf system running same refrigerant weight as R134a ( 1.7 kg) and compressor speed of 1500 rpm | Lower discharge pressure 0.4 – 1.0 bar Lower discharge line temperature 2-4K Higher suction pressure 0.17 -0.47 bar Different evaporator superheat range ±1.8K Lower sub cooling 4.5 – 4.8K Lower air TD across evaporator 0.7K

## Slide 10
R134a and R1234yf, condenser sub-cooling and evaporator super heat table
Unicla test - 1.7kg refrigerant charge at 1500rpm
Refrigerant operation
Ambient | Refrigerant type | Suction evaporator pressure | Condenser pressure | Suction evaporator temperature | Condenser temperature | Super heat | Sub-cool
25˚C | R134a | 1.92 bar | 10.35 bar | 8.70˚C | 37.10˚C | 8.70˚C | 9.90˚C
25˚C | R134a | 1.97 bar | 12.37 bar | 7.30˚C | 43.30˚C | 6.80˚C | 7.20˚C
25˚C | R134a | 1.94 bar | 12.97 bar | 6.30˚C | 45.20˚C | 6.30˚C | 7.05˚C
35˚C | R134a | 2.84 bar | 15.08 bar | 13.10˚C | 51.60˚C | 5.10˚C | 6.10˚C
35˚C | R134a | 2.85 bar | 17.52 bar | 15.40˚C | 58.30˚C | 7.40˚C | 5.95˚C
35˚C | R134a | 2.87 bar | 19.58 bar | 15.90˚C | 63.50˚C | 7.90˚C | 5.25˚C
25˚C | R1234-yf | 2.39 bar | 10.23 bar | 10.90˚C | 42.60˚C | 6.90˚C | 2.40˚C
25˚C | R1234-yf | 2.17 bar | 11.87 bar | 10.50˚C | 48.00˚C | 8.50˚C | 2.00˚C
25˚C | R1234-yf | 2.35 bar | 12.50 bar | 10.50˚C | 47.70˚C | 6.50˚C | 4.30˚C
35˚C | R1234-yf | 3.01 bar | 13.84 bar | 15.90˚C | 54.10˚C | 6.90˚C | 1.90˚C
35˚C | R1234-yf | 3.00 bar | 15.50 bar | 16.70˚C | 58.80˚C | 7.70˚C | 2.20˚C
35˚C | R1234-yf | 3.09 bar | 16.68 bar | 16.10˚C | 61.80˚C | 6.60˚C | 2.20˚C
Higher on low side
Lower on high side

## Slide 11
Standards
SAE International always at the forefront of MVAC design and innovation
Work commenced in 2003 for the search of an alternative to R134a
Dupont and Honeywell did the chemistry SAE took the lead on system design, component upgrades and risk assessment at the vehicles' level
Five key standards deal with new low GWP refrigerants R1234yf and R744 (CO2)

## Slide 12
References to 48 SAE standards
Refers to refrigerants R134a, R1234yf, R-744
Specifies design of fittings for R12 and R-152a
Passenger cars only (trucks and buses not included)
Prohibits use of any refrigerant rated less than A2L
Provides standards for design, assembly, testing and service to minimise environmental, health and safety impacts
SAE standard J639

## Slide 13
SAE standard J639- Service port fittings

## Slide 14
SAE standard J639- Service charge couplings

## Slide 15
SAE standard J639- Service fitting caps

## Slide 16
SAE standard J639 - R1234yf maximum working pressure
High side:
must not exceed 4.14 mPa (600 psig) gauge pressure during operation
must not exceed limit of any system component
pressure must be limited by compressor operation before relief valve on burst disc
Low side:
must not exceed 1.46 mPa (according to saturation pressure of R1234yf at 56°C) with system on or off
high pressure vapour
high pressure liquid
low pressure liquid
low pressure vapour

## Slide 17
SAE standard J639 - R1234yf maximum system burst pressure
High side:
new components must not be less than two times the working pressure of 8.24 mPA (1200 psig)
Low side:
new components must not be less than two times allowable pressure with system on or off – 2.92 (423psig) mPa
high pressure vapour
high pressure liquid
low pressure liquid
low pressure vapour

## Slide 18
SAE standard J639 - R1234yf maximum working temperature
High side:
discharge outlet at compressor and line must not exceed 150°C during continuous operation
discharge outlet must not exceed 160°C during intermittent (5 minute intervals) during operation
Low side:
must not exceed 56°C with system on or off
high pressure vapour
high pressure liquid
low pressure liquid
low pressure vapour

## Slide 19
SAE standard J639 - compressor design and requirements

## Slide 20
SAE standard J639 -
R1234yf maximum burst pressure of
compressor and adjacent cavities
Suction valve plate
Gasket

## Slide 21
SAE standard J639 -
R1234yf maximum burst pressure of
compressor and adjacent cavities
adjacent cavities (low side next to high side) shall be burst tested at maximum pressures
high side must be tested at twice the maximum high side working pressure which is 1200 psi (8.24 mPa) while the low side is maintained at 1.38 mPa
1200 psi (8.24 mPa)
200 psi (1.38 mPa)
1200 psi (8.24 mPa)
200 psi (1.38 mPa)

## Slide 22
SAE standard J639 - R1234yf compressor design requirements
must be inoperative with no power transmission or power if failed on drawing excessive torque
managed by lock sensor or permanent clutch cutout (designed to eliminate catastrophic failure of compressor components causing refrigerant leakage)
must have pressure relief < 4.14 mPa (600 psig) and self sealing

## Slide 23
SAE standard J639 -
R1234yf refrigerant line routing and connections
must be located outside the passenger compartment and outside the cabin airflow path (plenum) – or –
design to sufficiently present no leakage if inside the cabin or cabin air flow path
service manual must state a process to prevent any leakage into cabin or plenum
service fittings must have ease of access for technicians
piping must be sufficiently robust to withstand connect/disconnect procedures
high pressure vapour
high pressure liquid
low pressure liquid
low pressure vapour

## Slide 24
SAE standard J639 - R1234yf compressor design requirements

## Slide 25
SAE standard J639 - Internal heat exchanger
Internal heat exchanger (IHX)
Defined as a heat exchanger used to transfer heat between the low side pressure and high pressure flow circuits. Its function is to improve system capacity by further sub-cooling the refrigerant being supplied to the evaporator through the refrigerant control device.

## Slide 26
SAE standard J639 - internal heat exchanger (IHX)

## Slide 27
Suction line in (5-8°C)
Liquid line out
Liquid line in
Suction line out (15-20°C)
SAE standard J639
internal heat exchanger (IHX)
Peugeot 308 IHX
IHX- not insulated due to no sweating (the temperature never reaches the dew point)

## Slide 28
SAE standard J639 - internal heat exchanger (IHX)
R1234yf absorbs slightly less energy per unit of flow in a refrigerant cycle.
R134a absorbs 120.9 kj/kg
R1234yf absorbs 84.5 kj/kg
R1234yf

## Slide 29
SAE standard J639 - internal heat exchanger (IHX)

## Slide 30
SAE standard J639 - internal heat exchanger (IHX)
With extra subcooling of 10 – R1234yf absorbs 99.4 kj/kg
With extra subcooling of 15 – R1234yf absorbs 106.6 kj/kg

## Slide 31
SAE J2842
R1234yf and R744 design criteria and certification for OE mobile air conditioning evaporator and service replacements:
provides a testing framework for evaporator manufacturers to meet J639
describes labelling requirements
demands that all evaporator manufacturers build and test to this standard

## Slide 32
SAE J2842
requirements include standards for strength, corrosion, durability, fatigue resistance, burst pressure and design (2.92 mPa – 423psig)
must be labelled
must meet J639 as one of the MAC components
must never be repaired, re-worked or re-used
must have permanent label, stamp or etching
label must be two colour Pantone orange (151) and black